## Slide 1
“Reduce light emissions”
- simply let’s just do it!
Webinar “Erlebe die Finsternis” North Sea coast 2021-04-23
Andreas Hänel
Fachgruppe DARK SKY der VdS Kommission Lichtverschmutzung Astronomische Gesellschaft

## Slide 2
2
World heritage Wadden Sea
Leeuwarden Declaration, 2018

## Slide 3
3
Wadden sea: April 15/16 2021
at night:
cities
ships
oil platforms/wind farms
industry/ harbors
NASA/EOSDIS

## Slide 4
Ports Eastern Frisia
main light sources on coast (at 2 o‘clock)
connection to the islands (H – harbor)
but: no ferries at night!
Is it necessary to illuminate them all night long?
some are switched off –why not all?

## Slide 5
Villages
badly shielded
too bright (“light terror”)
color (insects)
within one village!
advertising all night long?
Notwendigkeit?

## Slide 6
Spa villages
glaring ship
ticket booth access beach
camping toilets
beach at 1 o’clock
is this necessary?????
Notwendigkeit?

## Slide 7
Pellworm: 3 nights in April 2015

## Slide 8
8
Public lighting
Full cut-off luminaires, 3000 K or less
160 lighting points switch-off at 22:30

## Slide 9
9
Restart in 2019
additional LEADER funding
biosphere project, sustainable tourism
exchange of 64 luminaires, 69 lamps
color temperature 2200 K (ultra warm white) insect friendly!
low light flux: 1000/1200, 5000 lm
switch-off 22:00

## Slide 10
10
Pellworm old harbor

## Slide 11
11
Pellworm private retrofit

## Slide 12
Pellworm: Zodiacal light

## Slide 13
13
Spiekeroog:
darkest sky
Utkieker looking at Gegenschein

## Slide 14
14

## Slide 15
15
Public lighting: Slurpad, beach and Nationalpark
exchange of extremely glaring 4000 K LED
View to East Nationalpark View to West

## Slide 16
16
Public lighting
67 + 15 public 3000 K LED
switch-off at 0:30
EN 13201: P4 -> 5 lx mean
  former: 10 – 22 lx max.
  new: 40 – 57 max
  30% reduction: 15 – 20 lx
Problem: uniformity 150 – 200 m distance

## Slide 17
17
Public lighting
reducing glare by a simple method
solution:
3300 lm -> 30% -> 990 lm

## Slide 18
Wall fixtures not shielded

## Slide 19
Flood lights
mount horizontally
max. 800 lm
≤ 3000 K

## Slide 20
Private luminaires (garden)
Solar lamps
hazardous waste
30 lx on soil!
max. 3000 K
use motion detector control!
avoid these luminaires!

## Slide 21
Illuminated ships
sailing
parking
Spiekeroog with comet NEOWISE

## Slide 22
Sustainable lighting
Is artifial light necessary? - prefer no light!
How much light is necessary? – low flux!
Where is the light necessary? – shield light!
When is light necessary? – reduce, adaptive!
Which quality of light? – low blue content!
Notwendigkeit?

## Slide 23
Sustainable lighting
saves money
is good for environment
is good for health
is easy
so: let’s do it!
Notwendigkeit?

## Slide 24
Thank you very much for your attention!
ahaenel@uos.de